## Slide 1
www.studymafia.org
Submitted To: Submitted By:
www.studymafia.org www.studymafia.org
Seminar
On
Perovskite Solar Cells
Notes: 1
1

## Slide 2: Content
Introduction
Origin and History
Basic Structure of a Photovoltaic Solar Cell
Three Generations of Solar Cells
Solar Perovskites
Methylammonium Lead Halide Perovskite
Chemistry of CH3NH3PbX3 solar perovskites
Fabrication and Laboratory preperation
Factors to be addressed
Replacing Lead with Tin
Conclusion
References

## Slide 3: Introduction
Perovskite is any mineral which has ABX3crystal structure, A and B are 2 cations of very different sizes and X is an anion that bonds to both.
Most Common type is crystal structure for CaTiO3 which is also known as Perovskite structure.
Synthetic Perovskites have been identified as possible inexpensive base materials for high - efficiency of up to 20%.
High future potential: PCE – boomed from 3.8% to 20%

## Slide 4: Origin And History
Perovskite was first discovered in the Ural mountains of Russia by Gustav Rose in 1839.
It was named after the Russian mineralogist Lev Perovski.
Found in the Earth’s mantle

## Slide 5: Basic Structure of a Photovoltaic Solar Cell
A photovoltaic solar cell is made of three main part:
  Light Absorber; converting incident photons to electron and holes
  Carrier Collector/s; capturing the carriers (electron and holes)
  Metal Contacts: transferring the carriers to the circuit
The heart of a solar cell is the absorber layer
Basic schematic of a photovoltaic solar cell

## Slide 6: Three Generations of Solar Cells
Wafer based:
  Monocrystalline silicon 25%
  Polycrystalline silicon 20%
  Multi-junction cell (different band-gap materials) 40%
Thin Films:
  Amorphous thin film silicon 13%
  CdTe (Cadmium Telluride) 17%
  CIGS (Copper Indium Gallium Selenium) 20%
Low Cost and high Efficient:
  DSSC (Dye-sensitized solar cells)
  QDSSC (Quantum Dot-sensitized solar cells)
  OPV (Organic photovoltics)
  QDs-Polymer Hybrid solar cells
  Perovskite Solar Cells
Highest efficiency

## Slide 8: What Are Solar Perovskites ?
All perovskites are not solar
Perovskite structured compound
‘Perovskite solar cell' is derived from the ABX3 crystal structure of the absorber materials
Most common perovskite absorber is methylammonium lead trihalide CH3NH3PbX3 (optical bandgap between 1.5 and 2.3 eV)

## Slide 9
Perovskite Systems
Inorganic Oxide Perovskites
Intrinsic Perovskites
Doped Perovskites
Halide Perovskites
Alkali-halide Perovskites A2Cl(LaNb2)O7
Organo-Metal Halide Perovskites

## Slide 10
Methylammonium Lead Halide Perovskites (MALX)
Hybrid Organic Inorganic Semiconductor Inorganic - Lead (Strong light absorption, Provide high efficiencies, even above 20 % as per NREL)
Organic- Methyl Ammonium (Soluble in Polar Solvents, provide low temperature processing - low cost and energy saving)

## Slide 11
Tuning the bandgap by adjusting the amount of halogen.
Introduce with Silicon cell for higher efficiencies.

## Slide 12: Chemistry of CH3NH3PbX3 solar perovskites
ABX3 Form
A- CH3NH3 and B- Pb and X- Halogen

## Slide 13
Degradation Factor
The instability of the Methyl Ammonium Lead Halide remains a major obstacle to commercialization.
In the presence of moisture, the perovskite undergoes rapid decomposition (15 hours to 2 days) which results in significant decline in device `performance.
Test Results reveal that unencapsulated perovskite solar cells reported in 80% drop in PCE over a 24h period.
Even more concerning is the decomposition to PbI2 because it is sparingly soluble in water and this would result in extreme toxicity.

## Slide 14
Replacing Lead with Tin

## Slide 15
Contd.
Normalized steady state photoluminescence (PL) with
photoexcitation at 500 nm, and absorption taken with reflectance and
transmission employing an integrating sphere of the tin-based and
lead-based perovskites CH3NH3SnI3 and CH3NH3PbI3 respectively.

## Slide 16
Conclusion
Lead?
Stability
Improving the PCE - more R&D

## Slide 17: References
www.google.com
www.wikipedia.com
www.studymafia.org
www.pptplanet.com

## Slide 18
THANKS