## Slide 1
www.studymafia.org
Submitted To: Submitted By:
www.studymafia.org www.studymafia.org
Seminar
On
Lathe Machine
Notes: 1

## Slide 2: Content
Introduction
History
Uses
Operations of Lathe Machine
Parts of the Lathe
Lathe Bed
Headstock
Quick-Change Gearbox
Carriage
Advantages
Types
Special Types of Lathes
Conclusion
References

## Slide 3: Introduction
Lathe is one of the most important machine tools in the metal working industry. A lathe operates on the principle of a rotating work piece and a fixed cutting tool.
The cutting tool is feed into the work piece, which rotates about its own axis, causing the work piece to be formed to the desired shape. Lathe machine is also known as “the mother/father of the entire tool family”.

## Slide 4: HISTORY
The lathe machine is one of the oldest and most important machine tools. As early as 1569, wood lathes were in use in France.
The lathe machine was adapted to metal cutting in England during the Industrial Revolution.
Lathe machine also called “Engine Lathe” because the first type of lathe was driven by a steam engine.

## Slide 5: USES
Wood Lathing
Metal Lathing
Acrylic Lathing

## Slide 6: Operations of Lathe Machine

## Slide 7: Operations of Lathe Machine…
Facing: This operation is almost essential for all works. In this operation, the work piece is held in the chuck and the facing tool is fed from the center of the work piece towards the outer surface or from the outer surface to the center, with the help of a cross-slide.
Plane Turning: It is an operation of removing excess amount of material from the surface the surface of the cylinder work piece.
Step Turning: It is an operation of producing various steps of different diameters of in the work piece. This operation is carried out in the similar way as plain turning.

## Slide 8: Parts of the Lathe

## Slide 9: Lathe Bed
Heavy, rugged casting
Made to support working parts of lathe
On top section are machined ways
  Guide and align major parts of lathe

## Slide 10: Headstock
Clamped on left-hand end of bed
Headstock spindle
  Hollow cylindrical shaft supported by bearings
    Provides drive through gears to work-holding devices
  Live center, faceplate, or chuck fitted to spindle nose to hold and drive work
Driven by stepped pulley or transmission gears
Feed reverse lever
  Reverses rotation of feed rod and lead screw

## Slide 11: Headstock…

## Slide 12: Quick-Change Gearbox
Contains number of different-size gears
Provides feed rod and lead-screw with various speeds for turning and thread-cutting operations
  Feed rod advances carriage when automatic feed lever engaged
  Lead screw advances the carriage for thread-cutting operations when split-nut lever engaged

## Slide 13: Quick-Change Gearbox

## Slide 14: Carriage
Used to move cutting tool along lathe bed
Consists of three main parts
  Saddle
    H-shaped casting mounted on top of lathe ways, provides means of mounting cross-slide and apron
  Cross-slide
  Apron

## Slide 15: Carriage…

## Slide 16: Advantages
Accuracy
Speed
Cost Effectiveness

## Slide 17: Types of Lathes
Engine lathe
  Not production lathe, found in school shops, tool rooms, and job shops
  Primarily for single piece or short runs
  Manually operated

## Slide 18: Special Types of Lathes
Turret lathe
  Used when many duplicate parts required
  Equipped with multisided tool post (turret) to which several different cutting tools mounted
    Employed in given sequence

## Slide 19: Special Types of Lathes…
Single- and multiple-spindle automatic lathes
  Six or eight different operations may be performed on many parts at the same time
  Will produce parts for as long as required
Tracer lathes
  Used where a few duplicate parts required
  Hydraulically operated cross-slide controlled by stylus bearing against round or flat template
Conventional/programmable lathe
  Operated as standard lathe or programmable lathe to automatically repeat machining operations

## Slide 20: Conclusion
Computerized Numerical Control (CNC) machining technology is a mouthful, but it is also fascinating by using computers to create metal parts and products for equipment and machines.
In more simple terms, it is high-tech machining technology.

## Slide 21: References
www.studymafia.org
www.google.com
www.wikipedia.com

## Slide 22: THANKS